PowerPod Trouble shooting guide

---
Is the PowerPod fully charged?
Are you using the supplied USB lead?

---
Is the mount fully secure with no movement?

---
Speed sensor must be on the front hub

---
Cadence sensor must be on none drive crankarm.
How is the battery life in the both speed and cadence sensors?

---
Have you paired the sensors to your Garmin 1ST?

---
Have you downloaded Issac for windows?

---
When connected Isaac software will recognise the powerpod
Not connected
Connected

---
Have you the latest Firm ware installed?

---
On setup choose your accuracy. For best accuracy a calibration ride is required. Please follow the instructions closely

---
Have you read and UNDERSTOOD the out and back instructions?

---
Before the calibration ride please watch the Powerpod installation video on Youtube
https://www.youtube.com/watch?v=--lDv-ecQSM

---
Recharging
Get into the habit of charging your Pod every 2nd ride, this will reduce the chance of the Pod running flat while out.
Please be aware that Power readings are not like readings from a speedometer,. They can fluctuate due to a number of factors.
After a recharge it is normal for the Powerpod to give abnormally high reading while it self calibrates. Readings will settle down after approximately 8mins

---
Like with all things electronic, the Powerpod requires setting up and will only perform to its maximum if the setup process if followed to the letter.
If in doubt, please always refer to the instruction manuals provided.